## Slide 1
UC
TECHNICAL BRIEFING / ENTERPRISE VOICE & COLLABORATION
Enterprise Voice with Cisco
Technologies, Contact Center
& Cloud Migration
From codecs and SIP signaling to CUCM configuration, contact center routing
and Webex migration — one complete expert lifecycle,
covering hardware, software, features and services.
Scope: voice protocols · Cisco Unified Communications Manager · UCCX / UCCE ·
Webex Calling & Contact Center · gateways & endpoints · configuration & operations
IP Phone
Voice GW
CUCM
call control
Webex Cloud
calling · CC
PSTN
Reference architecture used throughout this deck: endpoints register to CUCM,
gateways bridge the PSTN, and the Webex cloud provides the migration target.
Prepared for voice & collaboration engineering teams · 2026

## Slide 2
Contents
01
Voice Technology Foundations
Digitization, codecs, QoS budgets, CAC math, fax / modem relay, and full SIP / SDP anatomy
02
Cisco Unified Communications Core
Clusters, dial plan and numbering, provisioning, gateway & PRI configuration, trunks, security, media, paging, licensing
03
Collaboration Services & Endpoints
Unity Connection configuration, IM & Presence, endpoint families and registration, Expressway remote access
04
Contact Center Platforms
UCCX / UCCE / Webex CC configuration, IVR design, agent desktops, reporting, WFM and omnichannel
05
Cloud Migration
Webex Calling architecture, Control Hub, UCM Cloud, porting & E911, coexistence, timeline, five-year TCO
06
Operations & Troubleshooting
RTMT monitoring, signaling & media fault chains, DR & upgrades, TAC workflow, and a full incident case study
07
Expert Practice & Roadmap
Certification path, cutover checklists, capacity planning, design documents, automation, and the glossary
How to read this deck
Each content page states one conclusion in its title; the diagram, table or configuration on the page is the evidence.
Configuration excerpts are minimal but syntactically real IOS / CUCM patterns; adapt names and IPs to your environment.
Product capabilities follow Cisco documentation current as of early 2026.
Enterprise Voice with Cisco — Technologies, Contact Center & Cloud Migration

## Slide 3
01
Voice Technology Foundations
How analog speech becomes an IP packet stream, which codecs trade bandwidth for quality,
and why signaling and media are engineered as two separate planes.
Section 01 of 07 · Enterprise Voice with Cisco

## Slide 4
Every IP call is a codec choice: 64 kbps of fidelity or 8 kbps of efficiency
Nyquist sampling at 8 kHz and 8-bit quantization yield the 64 kbps PCM baseline; compression trades bandwidth against delay and quality.
From sound wave to RTP packet
Analog voice
300–3400 Hz speech band
Sampling
8000 samples / s (Nyquist)
Quantization
8 bits / sample → 64 kbps
Encoding
PCM or compressed codec
Packetization
20 ms frames typical
RTP / UDP / IP
sequence + timestamp
Bandwidth math (G.711, 20 ms frames): 64 kbps payload + RTP/UDP/IP overhead ≈ ~80–87 kbps per call on Ethernet. Over WAN links the overhead fraction grows — the reason CAC and codec policy exist.
G.711 is the LAN default: toll quality, no compression delay.
G.729 fits constrained WAN links at 8 kbps per call.
Opus adapts 6–510 kbps; standard in Webex and modern endpoints.
Codecs a Cisco engineer configures every week
Codec | Bit rate | MOS | Where it is used
G.711 | 64 kbps | ≈ 4.1 | LAN calls, fax/modem relay fallback, PSTN trunks
G.729 | 8 kbps | ≈ 3.9 | WAN links, branch sites under CAC pressure
G.722 | 64 kbps | ≈ 4.5 (wideband) | HD voice between capable endpoints
Opus | 6–510 kbps | ≈ 4.3+ | Webex Calling / Meetings, loss-adaptive internet paths
MOS = mean opinion score, the standard 1–5 perceived-quality scale. CUCM applies codec policy through regions (Section 02); transcoders and hardware DSP resources on gateways resolve mismatches between endpoints and trunks.
Basis: ITU-T G.711 / G.729 / G.722 recommendations; Cisco Collaboration SRND bandwidth and codec guidance, cisco.com

## Slide 5
Voice has hard media budgets: 150 ms one-way latency, 30 ms jitter, 1% loss
Exceed any one of the three budgets and MOS drops below toll quality — QoS exists to protect these numbers under load.
The three budgets and what breaks them
Metric | Budget | Typical cause when exceeded
One-way latency | ≤ 150 ms | long WAN paths, queued congestion, double media anchoring
Jitter | ≤ 30 ms | no priority queuing on congested links; buffer overruns
Packet loss | ≤ 1% | interface drops, policing, Wi-Fi interference
Why these numbers: beyond 150 ms one-way, talkers begin to interrupt each other; beyond 30 ms jitter, dejitter buffers underflow into lost speech; beyond 1% loss, G.711 has no concealment left and syllables drop.
The budgets come from ITU-T G.114 delay guidance and Cisco SRND quality targets; CMR data (Section 06) shows them per call.
How QoS defends the budgets on a Cisco network
1 · Classify and mark
voice media → DSCP EF, signaling → CS3; trust the phone's markings at the access-port trust boundary
2 · Queue with priority
LLQ / priority queue for EF on every WAN edge; signaling and media resources in CBWFQ classes
3 · Admit only what fits
CAC (locations / RSVP) blocks calls beyond the bandwidth budget instead of degrading all calls
Trust boundary, stated precisely: the access switch trusts DSCP from the phone's voice VLAN, rewrites markings from the PC data VLAN, and polices excess. One misconfigured port that trusts everything lets a single backup job destroy every call on the floor.
Basis: ITU-T G.114; Cisco Collaboration SRND and Enterprise QoS design guidance, cisco.com

## Slide 6
Bandwidth decides quality: per-call kbps times concurrent calls must fit the WAN budget
Every sizing conversation ends in one inequality — when it cannot hold, CAC blocks the extra call rather than ruining all of them.
Per-call bandwidth on Ethernet (20 ms frames)
Codec | Payload | On the wire (with overhead)
G.711 | 64 kbps | ≈ 80 kbps per call
G.729 | 8 kbps | ≈ 24 kbps per call
Opus (typical) | ~32 kbps | ≈ 40–48 kbps per call
Overhead = RTP/UDP/IP headers plus layer-2 framing; it dominates at low bit rates, which is why G.729's real-world saving is ~2.7×, not 8×. Header compression (cRTP) on slow links recovers much of it. On MPLS/VPN links add the tunnel overhead on top.
Worked example: one branch link
Branch voice budget: 1.5 Mbps of the WAN link. With G.729 ≈ 24 kbps per call, that is ≈ 60 concurrent calls; with G.711 ≈ 80 kbps, only ≈ 18. The location in CUCM is configured just below the safe number — the difference is headroom for bursts.
How CAC enforces the budget in CUCM
1. Every device belongs to a location (usually via its device pool); each location has a bandwidth figure toward every other location.
2. At call setup, CUCM subtracts the codec cost of the new call along the path; if any link would go negative, the call is rejected or rerouted.
3. Rejected calls can overflow to the PSTN via AAR — the caller hears reorder or the call completes over trunks instead.
4. RSVP-based CAC replaces static arithmetic with real network reservations.
Design rule of thumb: set the location bandwidth at about 80% of the engineered voice capacity of the link, review it after any WAN change, and alarm on CAC rejections — a rising rejection count is the earliest signal of a growing site.
Basis: Cisco Collaboration SRND — bandwidth and CAC chapters; per-call figures are standard SRND planning values for Ethernet

## Slide 7
Fax and modem traffic is the edge case that survives every migration: plan T.38 or bust
Alarm panels, elevators, and fax machines outlive every platform — they fail silently until the night of cutover.
Four transport options, in order of preference
Option | When and how
T.38 fax relay | real-time fax over IP; negotiated per call on the gateway / CUBE — the preferred path end to end
Fax pass-through | fax tones carried as G.711 audio; fallback when the far end lacks T.38 — demands a near-lossless path
Modem pass-through | alarms, elevators, legacy terminals; extremely loss-sensitive — G.711 only, clean QoS
Analog gateways | ATA 191 / 192 or VG-series FXS ports attach the analog device to IP telephony at all
Compression is the killer: never let fax or modem calls negotiate G.729 — modulated tones are not speech, and low-bitrate codecs destroy them. Pin G.711 or T.38 on the dial-peers that serve analog devices.
Cisco gateways switch echo cancellation and silence suppression off automatically when fax / modem tones are detected — verify, do not assume.
Design rules that keep the analog edge alive
1 · Inventory every analog line
elevators, fire panels, postage machines, security phones — they hide until cutover night
2 · Pin the codec and the relay
dial-peer codec g711ulaw with fax protocol t38 (or modem passthrough) on both legs
3 · Test with the real device
a successful test call with an analog simulator proves nothing about the actual alarm panel
Sometimes copper wins: elevator and fire-alarm lines carry code obligations and must work during power loss. Where regulation or risk demands it, keep a powered POTS line — that is a design decision, not a migration failure.
Basis: Cisco fax / modem over IP design guide; T.38 (ITU-T) relay and pass-through behavior on IOS gateways and CUBE

## Slide 8
Signaling sets up the call; RTP carries the voice — two separate planes
A SIP INVITE exchange negotiates the session; media then flows endpoint-to-endpoint (or via a gateway) independently of the call-control path.
A basic SIP call through CUCM
Phone A
CUCM
Phone B
INVITE 1001
INVITE 1001
180 Ringing
200 OK (SDP)
ACK
RTP media (end-to-end)
Signaling plane — INVITE / ringing / OK: routed through CUCM; failure blocks call setup.
Media plane — RTP stream: flows directly between endpoints (or via gateways / MTPs); failure degrades audio only.
The four protocols in a Cisco voice estate
Protocol | Role | Where Cisco uses it | Status today
SIP | Session setup, text-based, SDP negotiation | CUCM trunks, Webex Calling, endpoints | Default standard
H.323 | Legacy suite (H.225 / H.245) | Older video & gateway interworking | Legacy / phasing out
MGCP | Centralized gateway control | CUCM-controlled PSTN gateways | Mature, still deployed
SCCP | Cisco phone control ("Skinny") | Older IP phones on CUCM | Legacy; SIP preferred
Design consequence: every new integration — trunk, endpoint, contact center leg — should be specified as SIP first. MGCP and SCCP remain for installed estates, which is why migration plans (Section 05) inventory them before cutover.
Basis: IETF RFC 3261 (SIP); ITU-T H.323; RFC 3435 (MGCP); Cisco CUCM protocol support documentation, cisco.com

## Slide 9
A SIP call is six messages and an SDP contract — learn to read both
INVITE, ringing, answer and ACK set the call up; BYE tears it down; the SDP inside decides the media before anyone speaks.
The message ladder, annotated
Caller
CUCM
Callee
INVITE (SDP offer: codecs, IP, port)
100 Trying
180 Ringing
200 OK (SDP answer: one codec chosen)
ACK — call is live
RTP media — end-to-end, bypasses CUCM
BYE → 200 OK — teardown
Read SDL traces as this ladder: find the INVITE, follow the responses, and the failure's message names the failing layer.
The headers that answer troubleshooting questions
Header | What it tells you
Via | path each hop took — responses must retrace it; reveals proxies in the path
Call-ID + tags | the dialog's fingerprint — grep this to isolate one call in a busy trace
CSeq | message order within the dialog; out-of-sequence = retransmission or fork
Contact / RR | where to reach this party directly; Record-Route pins mid-dialog messages to proxies
4xx / 5xx / 6xx | failure class: 404 no route, 403 policy, 480/408 no answer, 503 capacity
SDP is the media contract
m=audio <port> RTP/AVP 0 8 101 offers G.711u / G.711a / RFC 2833; c= gives the media IP; a=sendrecv the direction.
The answer picks from the offered list — an empty intersection means codec mismatch and a transcoder or a failed call.
Early offer vs delayed offer decides when an MTP is inserted (Section 02).
Basis: RFC 3261 (SIP), RFC 4566 (SDP), RFC 2833 (DTMF events); CUCM SDL trace interpretation guides

## Slide 10
One UC core: CUCM at the center, with messaging, presence, edge and cloud around it
The reference estate below is the coordinate system for the rest of this deck — every configuration and migration step maps onto one of these blocks.
CUCM cluster
call control · dial plan · device registry
publisher + subscribers
Unity Connection
voicemail · unified messaging
IM & Presence
Jabber · presence · compliance
Expressway C / E
remote access · B2B calling
Voice gateways
ISR / Catalyst · PSTN, DSP, SRST
Endpoints
IP phones 8800 · Webex devices · Jabber
Contact center
UCCX · UCCE · Webex CC (Sec. 04)
Webex cloud
Webex Calling · Webex CC · migration target (Sec. 05)
SCCP / SIP
XMPP / SOAP
SIP TLS
MGCP / SIP
SIP / SCCP
SIP trunks
hybrid / migration link
— orange = call-control / media paths (critical) · — gray = service integration paths · dashed = cloud migration link
Basis: Cisco Collaboration System Solution Reference Network Design (SRND) architecture overview, cisco.com

## Slide 11
02
Cisco Unified Communications Core
CUCM cluster design, the dial-plan object hierarchy, gateway and trunk configuration,
and the survivability features that keep sites on the air when the WAN fails.
Section 02 of 07 · Enterprise Voice with Cisco

## Slide 12
One publisher holds the database; subscribers do the call work in 1:1 pairs
The cluster design separates configuration management from call processing, so a failed node never takes a whole site down.
Roles inside a CUCM cluster
Publisher — single read/write master of the configuration database (Informix); all admin changes land here and replicate to subscribers.
Subscribers — run the call-processing service; phones and gateways register to them; keep read-only database copies.
Redundancy groups — devices follow a CUCM group of up to three servers (primary / secondary / tertiary) and fail over automatically.
1:1 pairing — SRND practice: each active subscriber has an equal-capacity standby, so a node loss costs no calls.
What this means operationally
· Upgrades roll server-by-server; active pairs keep service up.
· Configuration is changed once on the publisher, never per node.
· Capacity planning counts registered devices per subscriber, not per cluster.
Deployment view: publisher + two 1:1 subscriber pairs
Publisher
config database · TFTP · admin
Sub 1 · active
call processing
Sub 2 · standby
takes over on failure
Sub 3 · active
call processing
Sub 4 · standby
takes over on failure
database replication
Phones · group A
Phones · group B
Up to 8 call-processing subscriber pairs per cluster; a single cluster serves on the order of 40,000+ devices when sized per Cisco SRND. Scale figures are release- and server-dependent — always validate against the SRND for your version.
Basis: Cisco Collaboration SRND — CUCM cluster design and redundancy sections; CUCM Administration Guide, cisco.com

## Slide 13
The dial plan is layered: partitions and CSS decide who may call what
Calling search spaces grant visibility into partitions; route patterns, lists and groups then steer the matched call to a gateway or trunk.
Object hierarchy a call traverses
Device + CSS
who is calling
Partitions
which numbers are visible
Route pattern
digit match, e.g. 9.1[2-9]XX[2-9]XXXXXX
Route list
ordered path preference
Route group
gateways / SIP trunks
PSTN / remote site
call leaves the estate
Policy lives at the top. A lobby phone gets a CSS that sees only internal partitions; an executive phone sees internal + local + international.
Routing lives at the bottom. Route lists give primary and overflow paths (e.g. SIP trunk → ISDN fallback) without changing patterns.
Toll fraud control is exactly this: restrictive CSS on trunks and devices, blocked patterns for premium prefixes.
Typical configuration objects (CUCM admin)
# Partition & calling search space
PT-Internal · PT-Local · PT-Intl
CSS-Employee = PT-Internal + PT-Local
# Route pattern (NANP, 9 = outside line)
9.1[2-9]XX[2-9]XXXXXX → PT-Local
# Path preference
RL-Outbound → RG-SIP-Trunk (primary)
→ RG-ISDN-GW (fallback)
# Bandwidth policy between sites
Region HQ ↔ Branch : G.729
Region HQ ↔ HQ : G.711
Regions and locations apply the codec policy from Section 01: regions set the codec per site pair, locations enforce call admission control (CAC) so WAN links are never oversubscribed.
Device pools bundle region, CUCM group, SRST reference and time zone — assign once per site, inherit on every phone.
Basis: Cisco CUCM Administration Guide — dial plan, partitions/CSS, route plan chapters; example patterns are illustrative NANP forms

## Slide 14
Normalize to +E.164 once at ingress; transform only at the edges
One canonical format inside the cluster keeps routing, voicemail and CDR consistent — presentation is a per-trunk concern.
The three zones of a disciplined numbering plan
1 · Ingress — globalize
gateway / trunk calling and called transformations convert whatever the carrier sends (10-digit, 7-digit, 4-digit) into +E.164 before CUCM routes
2 · Core — route globally
partitions, CSS and route patterns match one canonical form; identical numbers never mean two things; CDR, voicemail and directories all agree
3 · Egress — localize
called-party transformations strip the + and shape the digits each carrier expects; calling-party masks present the right caller ID per trunk
Why this matters in migrations: a cluster that normalized early moves to Webex Calling with a number inventory it can trust; a cluster full of local habits (9-outside, 4-digit inter-site, inconsistent caller ID) must fix its numbering before it can move anything.
Users still dial habits — 9 + number, extension to extension; translation patterns absorb the habit and emit +E.164.
The digit-manipulation toolbox
Tool | Job and example
Translation pattern | rewrite digits pre-routing; 9.1[2-9]XX[2-9]XXXXXX → +1\1\2\3 (absorb user dialing habit)
Called party xform | per route pattern at egress; +1312XXXXXXX → 312XXXXXXX for a carrier that wants 10 digits
Calling party mask | shape outbound caller ID; extension 4123 → +13125554123 via external phone number mask
Route list / group xform | trunk-specific transforms without touching patterns — one pattern, many carrier formats
Prefix / strip on gateway | POTS dial-peer strips the matched pattern by default; forward-digits or prefix restores what the PRI needs
The plus is literal: in CUCM patterns the + is part of the match, escaped as \+. Display numbers to users as +E.164, let translations convert to the local habit — never teach the core a habit.
Basis: CUCM dial-plan design guide — globalization with +E.164; ITU-T E.164 numbering plan

## Slide 15
Provisioning is templated: device pools and BAT turn 1,000 phones into a repeat
Hand-configuring phones does not scale; templates and the Bulk Administration Tool make provisioning a spreadsheet exercise.
The object chain every phone inherits
Device pool
site context: region, group, SRST
Phone / line templates
button layout, services, DN pattern
BAT job
CSV of users + phones + DNs
Registered phone
validated against the template
A BAT import, step by step
1. Export a sample CSV from BAT with the exact column set for the chosen template.
2. Fill users, MAC addresses, DNs and site codes — one row per phone, generated from your HR or asset data.
3. Upload, validate (dry run), then run the job; review the job log for rejected rows, fix and re-run only the failures.
4. Spot-check registrations in RTMT before shipping phones to desks.
5. Archive the CSV — it is the authoritative record of what was built, and the input to a future migration.
Hot-desking: provision people, not desks
With Extension Mobility, a user's DN, speed dials and services live in a device profile (UDP) that follows their login to any phone. Desks get generic phones; people get their identity on log-in — the same CSV discipline, applied to profiles instead of hardware.
Rule of thumb: anything you configure twice by hand belongs in a template. Device pool per site, phone template per model, line template per numbering range — after that, new sites are a copy and a find-replace.
Basis: Cisco CUCM Bulk Administration Guide and administration documentation, cisco.com

## Slide 16
Gateways bridge to the PSTN; SRST keeps a branch alive when the WAN fails
IOS gateways terminate T1/E1 or SIP provider trunks; survivable remote site telephony turns the branch router into fallback call control.
Three ways to control a gateway — choose SIP unless constrained
Mode | Strength | Constraint
SIP trunk | Full feature set, modern provider handoff | Dial plan logic lives in CUCM + IOS
MGCP | Centralized control, simple router config | Less flexible; D-channel backhaul
H.323 | Mature, feature-rich legacy interworking | More IOS-side dial plan to maintain
Survivability: what happens on WAN failure
Normal
phones → CUCM
WAN down
keepalives time out
SRST fallback
phones → router
Phones re-register to the branch router, which serves basic calling and PSTN access via local trunks. When the WAN returns, phones fall back to CUCM. Modern estates increasingly use SRST on Catalyst / ISR with SIP; sizing limits (max phones, DNs) are per platform — check the SRST version guide.
Minimal IOS voice configuration (ISR / Catalyst)
! SIP trunk toward provider
dial-peer voice 100 voip
destination-pattern 9T
session protocol sipv2
session target ipv4:203.0.113.10
codec g711ulaw
! inbound leg from CUCM
dial-peer voice 200 voip
destination-pattern 1...
session target ipv4:10.10.1.11
! survivability for the branch
voice register global
mode srst
max-dn 40 max-pool 20
! DSP resources for xcoder/conf
dspfarm profile 1 transcode
codec g711ulaw codec g729r8
Read it top to bottom: outbound peer matches the 9-prefix to the provider, inbound peer matches the 4-digit site range from CUCM, SRST caps registrations to the platform limit, and the DSP farm resolves codec mismatch and conferencing.
All IPs and patterns are placeholders — substitute your addressing.
Basis: Cisco IOS Voice Configuration Library — dial peers, SIP, SRST; configuration excerpt simplified for instruction

## Slide 17
A gateway config is three stanzas: voice service, the PRI, and matched dial-peers
Every IOS voice gateway reduces to the same skeleton; master the dial-peer matching order and most call failures become obvious.
Minimal working skeleton (ISR with T1 PRI)
voice service voip ip address trusted list ipv4 10.10.1.0 255.255.255.0 ! toll-fraud guard allow-connections h323 to sip controller T1 0/0/0 pri-group timeslots 1-24 interface Serial0/0/0:23 isdn switch-type primary-ni dial-peer voice 9100 pots description ** INBOUND FROM PSTN ** incoming called-number . direct-inward-dial port 0/0/0:23 dial-peer voice 2000 voip description ** TO CUCM SUB1 ** destination-pattern 2... session target ipv4:10.10.1.11 codec g711ulaw
Placeholder IPs and patterns — substitute your addressing. Add a second VoIP peer to the backup subscriber for failover.
Dial-peer matching — the order that decides everything
Rule | Behavior
inbound leg | matches incoming called-number → answer-address → destination-pattern → default peer 0, in that order
outbound leg | longest match on destination-pattern wins; preference breaks ties between peers
DID | direct-inward-dial uses the received digits as the outbound match — without it the caller gets a second dial tone
digit strip | POTS peers strip the matched pattern by default; forward-digits or prefix restores what the PRI needs
Two legs per call, always: one inbound match and one outbound match. When a call fails, ask which leg failed — then debug it:
debug isdn q931 · debug voip ccapi inout · debug ccsip messages
Debugs are loud — run them in a window with logging buffered and a filter, never blind on a production console.
Basis: Cisco IOS Voice Configuration Library — dial peers, PRI and voice service commands; excerpt simplified for instruction

## Slide 18
CUBE is the demarcation point: every external SIP call crosses the border element
The Cisco Unified Border Element terminates the provider trunk on your router — protocol interworking, security boundary and SIP normalization in one place.
What the border element does for you
Demarcation and security — the provider sees one controlled IP; your internal addressing and topology stay hidden; TLS/SRTP terminates here.
SIP normalization — SIP profiles rewrite headers, divert headers, and number formats so two SIP dialects interoperate without either side changing.
Media anchoring — RTP pins to the CUBE, enabling transcoding, DTMF interworking and lawful recording at the edge.
Connection management — dial peers steer inbound and outbound legs; survivability options keep local calling up if CUCM is unreachable.
Same box, two names: CUBE is the Cisco IOS XE function; "SBC" (session border controller) is the industry role. When a provider contract says SBC, they mean this layer — dedicated or combined on the site's ISR / Catalyst 8300.
Minimal CUBE excerpt (IOS XE)
! enable border element behavior
voice service voip
mode border-element
allow-connections sip to sip
sip
bind control source-interface Gi0/0/1
bind media source-interface Gi0/0/1
! outbound leg to the provider
dial-peer voice 10 voip
destination-pattern +1T
session target ipv4:198.51.100.20
voice-class sip profiles 100
dtmf-relay rtp-nte
codec g711ulaw
! normalize to E.164 for the provider
voice class sip-profiles 100
rule 1 request ANY sip-header
To modify "@(.*)>" "@\1>"
Two dial peers per call — one leg faces CUCM, one faces the provider; bind pins SIP and RTP to a known interface; the SIP profile is where last-resort interworking fixes live. IPs and patterns are placeholders.
Basis: Cisco CUBE configuration guide (IOS XE) and SIP trunk provider interoperability guides, cisco.com; excerpt simplified

## Slide 19
Voice security is layered: encrypt signaling and media, then control who may dial
Encryption protects confidentiality; dial-plan policy and edge control stop fraud — most real incidents are fraud, not eavesdropping.
The four layers, inside out
Device identity — every phone carries an LSC (locally significant certificate) issued by CAPF; the CTL file signs the config it downloads. No certificate, no registration.
Encrypted signaling and media — SIP over TLS between CUCM, phones and trunks; SRTP encrypts the voice stream itself. Enabled per security profile.
Toll-fraud policy — restrictive CSS on trunks and lobby devices, blocked premium-rate patterns, FAC / CMC codes for costly routes, and CDR alerting on anomalies.
Edge control — CUBE/SBC terminates external SIP with topology hiding, TLS, and call admission limits; firewall rules allow only the documented ports.
Why toll fraud gets the most attention
The classic attack chain: scan for exposed gateways or weak voicemail PINs → gain dial-out → generate premium-rate calls overnight. The cost lands on your trunk bill; the run is measured in hours, not weeks.
The controls that actually stop it are mundane: strong voicemail PIN policy, no unauthenticated dial-out on inbound trunk legs, blocked prefixes for premium and unusual international ranges, and after-hours call restrictions on unused devices.
Minimum hardening checklist
1 | Mixed-mode cluster security with CTL on every phone
2 | TLS trunks and SRTP where the far end supports it
3 | Block premium / unused international prefixes in route patterns
4 | Voicemail PIN minimums, lockout, no default passwords
5 | CDR anomaly report reviewed weekly (after-hours volume, odd destinations)
Basis: Cisco CUCM Security Guide and SRND security sections, cisco.com; fraud narrative is the industry-standard pattern, not a specific incident

## Slide 20
Media resources do what endpoints cannot: transcode, conference, announce, hold
When a call needs a capability an endpoint lacks, CUCM inserts a media resource — from software on the cluster or DSP hardware on gateways.
The four resource types and when they engage
Resource | Engaged when | Hosted on
Transcoder | codec mismatch, e.g. G.729 site ↔ G.711-only trunk | gateway DSPs (PVDM)
Conference bridge | ad-hoc or meet-me conference exceeds phone capacity | DSPs or CUCM software
MTP | DTMF / early-offer interworking on SIP legs | CUCM software or DSPs
Annunciator / MOH | system messages and music on hold streams | CUCM software
Placement matters: a transcoder in the wrong site forces media to hairpin across the WAN twice. Resources are grouped (MRG) and listed (MRGL), then assigned via the device pool — so the phone near the DSPs gets the DSPs.
The DTMF problem, in one box
DTMF interworking — phones send keypad digits as RFC 2833 / RTP-NTE events; some SIP legs expect KPML or in-band audio. When the two ends disagree, IVR menus silently fail: callers press digits and nothing happens. An MTP inserted on the trunk translates between the methods — the classic fix for "the menu doesn't work on external calls."
Hardware vs software, the honest trade
Software resources on CUCM cost no hardware but consume server CPU and handle only G.711 streams.
DSP resources on gateway PVDM modules handle any codec mix and large conference counts, but are finite — sessions are sized per module, so gateway DSP sizing belongs in the same capacity plan as trunk channels (Section 07).
Under-provisioned resources fail silently into user complaints: "conference won't start" or "call drops on transfer." Monitor session usage in RTMT before users notice.
Basis: Cisco CUCM media resources configuration and IOS DSP farm documentation, cisco.com

## Slide 21
Small features, loud failures: music on hold, call park, and paging
They carry no revenue and generate a steady share of tickets — because they touch multicast, partitions and legacy hardware at once.
The three features and their classic failure
Feature | How it works | Classic failure
Music on hold | MOH server streams unicast or multicast per device pool / MRGL; branches can source MOH from the gateway flash | silence on hold at branches — multicast routing (PIM) never enabled on the WAN
Call park | park DN ranges live in partitions; retrieval until the reversion timer rings the parking phone back | parked call vanishes — park range in a partition the retrieving CSS cannot see
Paging | no native paging in CUCM — InformaCast-style apps or FXS / loop-start adapters into ceiling amps | discovered at cutover — nobody scoped the warehouse and the fire-code paging zones
The reversion timer is the safety net: park reversion rings the parking phone back after (typically) 60 seconds — a parked call can be forgotten, never lost, when reversion and its CSS are right.
Directed park with BLF monitoring lets receptionists see parked calls as line states — configure the BLF speed-dial list in the phone button template.
Configuration checkpoints before go-live
MOH per device pool
audio source uploaded once; MRGL decides unicast vs multicast per site; gateway moh multicast for SRST branches
Multicast boundary
PIM sparse mode on the path; scope the MOH group so it never floods the WAN — test with a branch phone on hold
Park DNs and reversion
unique park ranges per site in the right partition; reversion destination reachable from every phone that parks
Paging adapter FXS
auto-answer the paging extension on the FXS port; zone the amps physically; document zones in the LLD
Design rule: park ranges, MOH sources and paging zones are site design data — they belong in the LLD next to the dial plan, not in someone's memory.
Basis: CUCM feature configuration guide — MOH, call park and directed park; multicast routing per IOS IP multicast documentation

## Slide 22
Licensing is a design dependency: it decides what you may deploy before you deploy it
Smart Licensing, Flex and Webex subscriptions each count differently — model them in the bill of materials, not at install time.
The four models you will actually meet
Model | What it counts | Watch for
Smart Licensing | on-prem CUCM 12.5+, Unity, Expressway register to CSSM; user/device tiers | out-of-compliance blocks config adds; air-gapped sites use Specific License Reservation
Flex Plan | subscription covering on-prem and cloud as Knowledge Workers | portability between deployment models — the migration-friendly path
Webex subscription | named users and workspaces in Control Hub; features per location | true-up model; auto attendants and queues are licensed per location
UCSS / ESW legacy | upgrade coverage for perpetual licenses | expired coverage means no upgrade rights — check before planning an upgrade
Flex earns its place during migration: the same subscription follows users from on-prem CUCM to Webex Calling, so moving waves does not mean buying licenses twice — confirm portability terms with the account team before phase 1.
What a defensible license count includes
Users by tier
essential (analog/common) vs enhanced vs CUWL — tier by actual feature use, not job title
Shared and adjunct devices
lobby phones, conference rooms, second devices per user — the line that surprises every BOM
Contact center agents
UCCX / UCCE agent licenses are counted separately from UC users — peak concurrent, not named
BOM discipline
License count = users × tier + shared workspaces + adjunct devices + peak agents, plus ~10% growth. Write the formula into the HLD so the count can be re-derived, not remembered.
Enterprise agreements (CLA) trade per-unit precision for simplicity — still model the true-up date.
Basis: Cisco Smart Licensing, Collaboration Flex Plan and Webex subscription documentation, cisco.com; tiers as published

## Slide 23
03
Collaboration Services & Endpoints
Messaging, presence and edge services around the core; the phones, soft clients and
firmware users actually touch; and VPN-less remote access through Expressway.
Section 03 of 07 · Enterprise Voice with Cisco

## Slide 24
Beyond call control: messaging, presence and edge services complete the UC stack
Each service attaches to CUCM through a defined protocol and adds one class of user-visible capability — configure them in this dependency order.
Service | What it adds | Attaches via | Key config items
Unity Connection | Voicemail, unified messaging to email, auto-attendant | SCCP / SIP ports on CUCM; MWI | VM ports, templates, COS
IM & Presence | Jabber chat, desk-phone control, presence states | SIP trunk + CTI; XMPP to clients | Service profiles, UC services
Expressway C/E | Mobile & remote access without VPN; B2B SIP/H.323 | SIP trunk to CUCM; traversal zone pair | Zones, certs, search rules
CDR / CMR + RTMT | Call records, quality metrics, alarms and traces | Service activation on CUCM nodes | Billing servers, trace levels
Dependency order in practice: cluster services and device pools first, then voicemail integration, then IM&P/Jabber, then Expressway for off-net users — each layer assumes the previous one registers cleanly. CDR/CMR is enabled from day one; you cannot troubleshoot quality retroactively without it.
Definition — MWI
Message waiting indicator: the lamp / stutter dial tone Unity Connection toggles through CUCM when a voicemail arrives. The classic first test of a voicemail integration.
Feature services on CUCM itself
· Extension Mobility — user profile follows login
· Hunt groups & call pickup teams
· Music on hold and ad-hoc conferencing
· Single Number Reach / mobile connect
· Call recording via SIP trunk to recorder
· TLS / SRTP phone security (CTL, LSC)
Basis: Cisco Unity Connection, IM & Presence, Expressway and CUCM feature configuration guides, cisco.com

## Slide 25
Endpoints are the visible half of voice: models, firmware and registration states
Every user judgment of "the phone system" is really a judgment of its endpoints — choose, load and manage them deliberately.
The four endpoint families in a Cisco estate
Family | Where it fits | Registers to
IP Phone 8800 | desks; Enterprise or MPP firmware variants | CUCM (Enterprise) / Webex (MPP)
Webex devices | Desk / Room series, video-first shared spaces | Webex cloud or CUCM
Jabber / Webex app | softphone on PC and mobile; remote workers | CUCM + IM&P / Webex
ATA / VG gateways | analog holdouts: fax, paging, door phones | CUCM via SCCP / SIP
Firmware is lifecycle policy: CUCM ships device loads; the device defaults list controls which version phones download from TFTP. Stage new firmware on a pilot device pool first — a bad load is a site-wide outage you caused yourself.
MPP phones convert between on-prem and Webex registration, making them the endpoint of choice for estates that expect to migrate (Section 05).
Registration, state by state
1 · Power and network — PoE up, voice VLAN from CDP/LLDP, DHCP address with option 150 (TFTP server).
2 · Config download — phone fetches its signed config file from TFTP; CTL validation happens here.
3 · Register — SIP or SCCP registration to the primary subscriber in its CUCM group; keepalives maintain the session.
4 · Serve calls — softkeys, lines and services come alive; failures at each stage have distinct status messages on the phone's web page.
Field habit: the phone's built-in web status page (browse to its IP) shows network, TFTP and registration status with plain-language error messages — it answers "why won't this phone register" faster than any server log.
Basis: Cisco IP Phone 8800 series and Webex devices administration documentation, cisco.com

## Slide 26
Expressway delivers full UC off-net without VPN — zones are the trust design
Mobile and Remote Access (MRA) lets Jabber and desk phones register from anywhere; the traversal zone pair is what makes it safe.
The MRA path from the internet to the core
Internet
Jabber / phone
off-net user
Expressway-E
DMZ edge
Expressway-C
inside
CUCM · IM&P Unity Connection
SIP TLS
traversal zone
SIP TLS
The traversal zone is a mutually authenticated, always-on tunnel between the E (DMZ) and C (inside) pair. No inbound ports are opened to the core; the C initiates everything. Certificates are the whole trust model — public CA on the E, and both nodes must trust each other.
What you actually configure
· Domains and DNS SRV records (_collab-edge._tls)
· Traversal zone pair between E and C, with certificates
Beyond MRA
B2B calling — SIP/H.323 calls between organizations, with search rules and rich media sessions.
Webex hybrid — the same pair hosts hybrid calendar and call connectors toward the cloud.
Business continuity — remote workers keep full dialing behavior when offices close; no VPN capacity needed for voice.
Basis: Cisco Expressway basic configuration and MRA deployment guides, cisco.com

## Slide 27
Unity Connection is five objects: ports, templates, users, handlers, and MWI
Voicemail looks simple because the complexity hides in the call handlers and the class of service.
The five objects, in build order
Object | What it carries
1 · VM ports / trunk | SCCP port group or SIP trunk to CUCM, plus the voicemail pilot and hunt pilot — the integration itself
2 · User templates | class of service, mailbox quotas, notification devices — every new mailbox inherits from one
3 · Users / mailboxes | imported from CUCM via AXL or from LDAP; alias and extension must match the dial plan
4 · Call handlers | the auto attendant — greetings, caller-input menus, transfer rules; most custom work lives here
5 · MWI on / off DNs | the message-waiting lamp pair; must be reachable from every phone's CSS
The classic interview question: why does MWI work for some phones and not others? Because the MWI DNs sit in a partition — if a phone's CSS cannot reach them, Unity lights the lamp and CUCM cannot deliver it.
Beyond the five objects
VPIM networking
site-to-site voicemail exchange, and the bridge to legacy voicemail during a migration — users reply across systems
Unified messaging
single inbox sync to Exchange / O365 — voicemail appears as email; deletions stay in sync both ways
Personal call transfer rules
the find-me feature users love — time-of-day rules cascade desk, mobile, home; keep the PSTN hop secured
Troubleshooting pair: the Port Status Monitor shows every port's live state — a call stuck ringing into voicemail is a port problem until proven otherwise. Run the MWI sync task after any cluster failover.
Backups ride the same DRS schedule as CUCM (Section 06) — voicemail loss is a data incident, not a voice incident.
Basis: Cisco Unity Connection administration and integration guides, cisco.com; VPIM per RFC 3801

## Slide 28
04
Contact Center Platforms
Choosing between UCCX, UCCE and Webex Contact Center by scale and operating model,
and the end-to-end path every routed contact takes from IVR to wrap-up.
Section 04 of 07 · Enterprise Voice with Cisco

## Slide 29
Three platforms, three scales: UCCX for SMB, UCCE for enterprise, Webex CC for cloud
The selection variable is not features — all three route and queue — but agent count, customization depth, and who operates the platform.
 | UCCX | UCCE / PCCE | Webex Contact Center
Typical scale | up to ~400 agents | thousands of agents, multi-site | elastic; from small to very large
Deployment | on-prem VMs with CUCM | on-prem / private cloud, dedicated infra | Cisco-operated public cloud
Routing engine | CCX scripts (IVR + skills) | ICM scripts, enterprise-wide | cloud flow builder, omnichannel
Agent desktop | Finesse (browser) | Finesse (browser) | Webex Agent Desktop
Reporting | CUIC historical + live | CUIC + HDS, deep historicals | Analyzer (cloud analytics)
Best fit | single-site helpdesks, simple queues | regulated enterprise, complex routing, legacy integration | cloud-first estates, hybrid agents, Webex Calling users
Migration signal: organizations already on UCCX/UCCE increasingly adopt Webex CC first for new lines of business, then port legacy queues in waves — the phased pattern detailed in Section 05.
Shared plumbing: all three consume the same voice foundation — SIP trunks, gateways, codecs, QoS. Skills built in Sections 01–02 transfer directly; what changes is who owns the servers.
Basis: Cisco UCCX / UCCE product documentation and Webex Contact Center data sheet, cisco.com and help.webex.com, early 2026

## Slide 30
UCCX configuration is six objects deep: from application to agent skill
A working queue is a chain of objects, each with exactly one job — build them in order and troubleshoot them in order.
The object chain behind one working queue
Application + trigger
Script
prompts, menus, queue logic
CSQ
contact service queue, skill criteria
Skills & resources agents with competence levels
Team & desktop supervisor scope, Finesse layout
Read the chain both ways: a call arrives at the trigger and flows right; a complaint ("calls queue but no agent rings") is diagnosed walking left from the agent — is the agent in Ready, skilled on the CSQ, and does the script select that CSQ?
Where each piece is configured
Object | Console
Triggers, ports, route point | CUCM + CCX Administration (JTAPI)
Scripts | CCX Editor (desktop tool)
CSQs, skills, teams | CCX Administration web
Agent / supervisor desktops | Finesse Administration (layouts, reasons)
Reports | CUIC — live data and historical
Two operational facts to remember
UCCX runs as an HA pair — publisher and subscriber failover automatically, but CTI ports and agent sessions re-establish; brief pauses during failover are normal and should be rehearsed.
Every UCCX release pairs with specific CUCM versions — check the compatibility matrix before upgrading either side; an unsupported pair loses the JTAPI link and the whole contact center goes quiet.
Basis: Cisco UCCX administration, scripting and compatibility documentation, cisco.com

## Slide 31
Every contact follows the same path: qualify in IVR, route by skill, serve, measure
The stages below are identical in concept across UCCX, UCCE and Webex CC — only the component names change.
1 · Inbound
PSTN trunk → gateway / CVP
2 · IVR qualify
menu, ID capture, self-service
3 · Route & queue
skill match, priority, callback
4 · Agent serve
Finesse / Agent Desktop + screen pop
5 · Wrap-up & measure
codes → CUIC / Analyzer
Where configuration effort actually goes
IVR / self-service — CCX editor scripts or CVP Studio / cloud flows: prompts, DTMF, database dips, speech recognition. This is where most caller experience is won or lost.
Skills & queues — map agents to skill groups with competence levels; CSQs (UCCX) or precision queues (UCCE) decide who rings first.
Desktop — Finesse layouts, screen-pop URLs into CRM, wrap-up codes, reason codes for not-ready states.
Omnichannel — email, chat and social route through the same skill logic in Webex CC and UCCE digital channels.
Definition — screen pop
Caller data collected in IVR (account number, menu choice) is passed with the routed call and opens the matching CRM record on the agent's desktop at answer time. It removes the "can you repeat your account number" step and typically saves 15–30 seconds of handle time per call.
Reporting closes the loop. Every stage writes records — offered, handled, abandoned, service level, AHT — into CUIC (on-prem) or Analyzer (Webex CC). Workforce management and quality/recording (Calabrio or Webex WFO) consume the same data for staffing and coaching.
Basis: Cisco UCCX / UCCE scripting and Finesse documentation; Webex Contact Center setup guide, help.webex.com

## Slide 32
Self-service lives in the IVR: prompts, digits and database dips decide deflection
The IVR is software with a caller on the other end — its building blocks are few, but its design rules are unforgiving.
The six blocks every script is built from
Block | What it does
Play prompt | recorded or TTS audio; every second costs patience
Get digits / menu | DTMF capture with timeout and error branches
ASR / TTS | speech recognition and synthesized prompts
Database dip | lookup by ANI / entered ID → route or self-serve
Queue / transfer | hand the contact to a CSQ, callback, or external number
UCCX scripts these in the CCX Editor; UCCE does the same at enterprise scale with CVP Call Studio rendering VXML on the voice gateway; Webex CC uses the cloud flow builder. The grammar of prompts, digits and dips is identical across all three.
Design rules that survive contact with real callers
Depth ≤ 3 menus. Every additional level loses a measurable share of callers to abandonment or zero-out.
Always offer escape. A path to an agent — stated, not hidden — reduces repeat calls more than any prompt polish.
Offer callback at peak. Virtual hold preserves the caller's place without their minutes on the line.
Authenticate early, once. ID captured in the IVR must travel with the call (screen pop, Section 04), never be re-asked.
Measure the IVR as a product: track containment rate (resolved without an agent), zero-out rate, and average time in IVR per menu. A "contained" call that fails and makes the customer call back is a double cost, not a saving.
Basis: Cisco UCCX scripting guide, CVP Call Studio documentation and Webex CC flow documentation; design rules are editorial guidance

## Slide 33
The agent desktop is an integration surface: gadgets, screen pops and APIs
Finesse is not a phone with buttons — it is a browser container where telephony, CRM and workflow meet at answer time.
Finesse architecture in one view
Agent browser
Finesse desktop + gadgets
Finesse server
REST APIs · CTI events · XMPP
CC engine + CUCM
routing, agent state, calls
CRM / ITSM
Salesforce · Dynamics · ServiceNow
URL pop / gadget
Three integration patterns: a URL screen pop opens the CRM record in a frame at answer; an embedded gadget runs CRM logic inside Finesse; a packaged connector (Cisco or CRM-vendor) puts call controls inside the CRM itself — increasingly the preferred direction.
Desktop items you configure, and why
Item | Why it matters
Layout per team | each role sees the gadgets and queues it uses
Wrap-up codes | structured outcomes feed reporting and callbacks
Not-ready reasons | coaching needs "training" separate from "avoiding"
Workflows / pop rules | data from IVR lands in the right CRM field
Adoption rule: agents judge the contact center by their desktop, not the platform. Involve two working agents in layout design; a desktop they help build is a desktop they will use correctly — including wrap-up discipline.
Basis: Cisco Finesse administration and developer documentation; CRM connector documentation, cisco.com

## Slide 34
Reporting closes the loop: offered, handled, service level and AHT drive staffing
Contact center metrics have precise definitions — agree on them before comparing dashboards across teams or platforms.
The six metrics, defined exactly
Metric | Definition
Offered | contacts presented to a queue (includes abandoned)
Handled | contacts connected to and completed by an agent
Abandon rate | offered − handled, ÷ offered; watch the time-to-abandon curve
Service level | % answered within threshold, e.g. 80/20 = 80% in 20 s
AHT | average handle time = talk + hold + wrap-up, per contact
Occupancy and ASA complete the set: occupancy = agent time on contacts ÷ staffed time (sustained values above ~85% burn teams out); ASA = average speed of answer, the caller-felt twin of service level.
The tooling chain behind the numbers
CUIC (on-prem) — live dashboards for supervisors plus historical reports; UCCE adds the HDS database for long-term, SQL-level history.
Analyzer (Webex CC) — cloud historicals and visualizations with data retention set by your subscription.
WFM + QM — Calabrio or Webex WFO forecast volumes, build schedules from AHT/SL targets, and score recorded calls for coaching.
Definition — Erlang thinking
Traffic intensity is measured in erlangs: with λ calls per hour. Erlang C converts E and a service-level target into the required agent count; Erlang B sizes trunk channels. Both appear again in capacity planning (Section 07) — the same mathematics, one for people, one for circuits.
Definition — Erlang thinking
Traffic intensity is measured in erlangs: \(E = \frac{\lambda \times AHT}{3600}\) with λ calls per hour. Erlang C converts E and a service-level target into the required agent count; Erlang B sizes trunk channels. Both appear again in capacity planning (Section 07) — the same mathematics, one for people, one for circuits.
Basis: Cisco CUIC reporting documentation and Webex CC Analyzer documentation; metric definitions follow standard contact center practice

## Slide 35
Digital channels reuse voice logic: one routing brain for chat, email and social
Omnichannel is not more queues — it is the same skill-based engine fed by more front doors, with agents blending media by design.
Channel support across the three platforms
Channel | Webex CC | UCCE | UCCX
Voice | native | native | native
Chat / messaging | native digital | via ECE or partner | limited
Email | native digital | via ECE or partner | limited
SMS / social | native digital | partner integration | no
The cloud platform's advantage here is structural: digital channels arrive as built-in flows in Webex CC, while on-prem estates bolt them on. For digital-heavy roadmaps this table, not the voice table, decides the platform question (Section 05).
Blending changes how you staff
Concurrency is a policy — an agent may handle several chats but one call; the engine caps simultaneous contacts by channel.
Voice preempts — inbound calls interrupt lower-priority digital work, not the other way around; the routing engine enforces it.
AHT differs per channel — staff forecasts must be built per media type, then blended; one average AHT mis-staffs both.
Where AI fits today
Virtual agents front the IVR with natural-language intent capture; agent-assist transcribes calls live and suggests answers and next actions; post-call AI generates summaries that cut wrap-up time. All three exist in the Webex CC ecosystem and through partners on-prem — evaluate them on measured AHT and containment, not demos.
Basis: Webex Contact Center digital channels documentation and Cisco ECE documentation, cisco.com / help.webex.com, early 2026

## Slide 36
Webex Contact Center moves the same six blocks into a browser flow builder
Entry point, flow, queue, team — the vocabulary changes, the queueing mathematics does not.
The configuration chain, left to right
Entry point
DNIS number mapped to a flow
Flow
drag-and-drop IVR: play, menu, collect, HTTP dip
Queue
routing profile, distribution, overflow
Team
agents grouped under a site
Agent desktop
Webex Agent Desktop, layout per team
Analyzer
reports and dashboards close the loop
The flow builder is the CCX editor's successor: the same blocks from Section 04 — prompts, menus, data dips, queue and transfer — exist as nodes on a canvas, versioned and published like software, with a validation pass before a flow can go live.
Digital channels (chat, email, social) enter the same queues through multimedia profiles — one routing brain for every channel, as on the omnichannel page.
What you configure beyond the chain
Component | Configuration
Analyzer | stock and custom reports, dashboards, scheduled exports — the CUIC successor
WFO / QM | recording, scorecards and forecasting via Calabrio or Webex WFO integrations
Virtual agent | natural-language front end to the flow; escalates to a queue with full context
Agent assist | live transcription, suggested responses, automatic wrap-up summaries
APIs / webhooks | provisioning APIs and agent-state events — the same automation story as Section 07
The math did not move: staffing is still Erlang C against offered load and AHT (Section 07). A cloud console changes who operates the platform, not how many agents Tuesday needs.
PSTN for entry points rides Webex Calling trunks (Section 05).
Basis: Webex Contact Center setup and flow-builder documentation, help.webex.com

## Slide 37
05
Cloud Migration
Moving users, dial plan and PSTN access from on-prem CUCM and contact center to Webex
in gated phases — with a rollback position at every gate.
Section 05 of 07 · Enterprise Voice with Cisco

## Slide 38
Migration is phased: assess, pilot, port numbers in waves, then decommission
Users and directory move first, PSTN follows site by site, and the old cluster stays warm until the last wave proves out.
Five phases, each with a go/no-go gate
0 · Assess
inventory devices, DNs, trunks, licenses; find analog/fax, legacy SCCP, features in use
1 · Pilot
50–200 friendly users on Webex Calling; validate QoS, E911, calling plans
2 · Site waves
users migrate per site; hybrid period uses dial-plan integration between CUCM and Webex
3 · PSTN port
number porting to Cisco Calling Plans or move trunks to local gateways
4 · Decommission
drain CUCM/UCCX; archive CDRs; cancel circuits; retire VMs and gateways
Gate discipline: each phase ends with objective checks (registration rate, MOS on test calls, E911 test, port completion report) and a documented rollback — for phases 1–3 rollback is simply "users stay on / return to CUCM," because the old cluster remains the system of record until phase 4.
PSTN access after migration: three supported options
Option | How it works | Best when
Cisco Calling Plans | PSTN bundled by Cisco; numbers ported into Webex | covered countries, simple estates
Local Gateway (LGW) | your SIP provider terminates on an on-prem gateway registered to Webex | existing contracts, special trunks
Cloud Connect | certified carrier peers into Webex on your behalf | global carriers, no on-prem hardware
Contact center follows the same logic: new queues are built in Webex CC while UCCE/UCCX keeps running; calls can hairpin between the two during coexistence.
A hybrid steady-state is legitimate — many estates keep a small on-prem footprint for fax, paging or regulated trunks indefinitely.
Basis: Webex Calling migration and Local Gateway documentation, help.webex.com; Cisco UCM Cloud migration guides, cisco.com

## Slide 39
Webex Calling is cloud call control with local breakout: locations define the edges
Cisco runs the call control in regional data centers; your network supplies endpoints, PSTN breakout and the management plane.
The architecture, top to bottom
Control Hub
management plane (browser)
Webex Calling cloud
regional data centers · call control
voicemail · media services
Endpoints
MPP phones · Webex app
Local Gateway (LGW)
your IOS XE router, per location
PSTN
carrier / SIP provider
SIP TLS registration
SIP trunk (registered)
local PSTN
Locations are the design unit: every site is a location with its own PSTN connection choice (Calling Plans, LGW, or Cloud Connect), bandwidth policy, and emergency-calling settings. Endpoints register to the nearest regional cloud; media stays as local as the PSTN breakout allows.
Survivability
An on-prem survivability gateway keeps local calling and PSTN access alive if the cloud path fails — the cloud-era successor to SRST.
Basis: Webex Calling architecture, Local Gateway and survivability documentation, help.webex.com

## Slide 40
Control Hub is the Webex operating console: users, locations, numbers, features
Day-two administration is a browser workflow — single edits, CSV bulk jobs, or directory synchronization keep one source of truth.
What you administer, and where it lives
Object | Managed attributes | Typical task
Users & workspaces | licenses, numbers, extension, caller ID, calling behavior | add user, assign Calling license
Locations | PSTN choice, bandwidth policy, emergency settings | create site, attach trunk
Phone numbers | inventory, assignment state | reserve, assign, port in
Features | voicemail, auto attendant, hunt group, call queue, recording | configure per location
Devices | MPP phones, ATA, room devices | add by MAC or activation code
Role-based access: full, read-only, and location-scoped administrator roles map to real support tiers — a site administrator can manage their location without touching global settings.
Audit logs record every change with actor and timestamp; treat them as part of the compliance trail during migration waves.
Three provisioning paths, scaled to the job
1 · Manual — the single user
add user → assign license → assign number → done; the right tool for day-two changes
2 · CSV bulk — the migration wave
one template provisions hundreds of users, numbers, and workspaces per job; errors return as a row-level report
3 · Directory sync — the steady state
Directory Connector (AD/LDAP) or Azure AD sync makes the directory authoritative; Control Hub stops being a user database
Licensing in one line
Professional licenses attach to named users; workspace licenses serve common-area devices. Auto attendants and call queues are licensed per location — plan them with the location design, not per user.
Basis: Control Hub administration, user and workspace management guides, help.webex.com

## Slide 41
Three call-control homes, three operating contracts — decide who runs what
On-premises CUCM, hosted UCM Cloud, and Webex Calling differ less in features than in where the responsibility boundary sits.
Aspect | CUCM on-premises | UCM Cloud (hosted) | Webex Calling (SaaS)
Servers and upgrades | you or your integrator | Cisco or partner operates | Cisco operates
Hardware and data center | your UCS, your DC | provider data center | Cisco cloud regions
Dial plan control | full — CSS, partitions, route logic | full — same constructs | location-based, deliberately simpler
PSTN access | your trunks via CUBE / gateways | your trunks or provider | Calling Plans, Local Gateway, Cloud Connect
Endpoints | full 8800 / MPP / Jabber range | same as on-premises | MPP phones, Webex app, ATA
Survivability | SRST at the branch | SRST at the branch | survivability gateway
Best fit | complex dial plans, strict control, heavy compliance | keep CUCM logic, shed hardware | standardize, cloud-first, elastic scale
Migration reality: UCM Cloud preserves your dial-plan logic almost one-to-one; Webex Calling rewards redesign. Do not replicate legacy partition trees into locations — carry over the call flows users actually use, and let the rest retire.
Basis: Cisco UCM Cloud and Webex Calling solution overviews, cisco.com; responsibility boundaries as documented per offer

## Slide 42
Number porting and emergency calling are the top risks — both are testable gates
None of these risks is discovered late if the assessment phase is honest; each has a concrete validation step before the wave proceeds.
Risk | Severity | Mitigation | Validation gate
Number porting delays | high | order ports early; keep old trunks live during transition; stage a temporary DID redirect | port completion + inbound test calls per range
E911 / emergency routing | high | location database per site; ELIN mapping; regulatory check per country | 933/911 test call from each site
Analog & fax devices | medium | ATAs / VG gateways; T.38 relay for fax; keep minimal ISDN for elevators/alarms | per-device functional test list
WAN / QoS readiness | medium | bandwidth per concurrent call (Opus adaptive); DSCP EF marking end-to-end | load test with MOS ≥ 4.0 at peak
Feature parity gaps | medium | map used CUCM features to Webex equivalents; script workarounds for hunt/paging | signed feature-mapping document
CC integration & reporting | medium | rebuild CRM screen pops and WFM feeds against Webex CC APIs before queue cutover | parallel-run one queue for 2 weeks
The pattern to notice: every mitigation ends in a test that can fail — inbound calls, a 911 test, a fax page, a load test. A migration plan without failure-capable gates is a schedule, not an engineering plan.
Basis: Webex Calling migration best practices and emergency-calling configuration guides, help.webex.com; severity ratings are editorial guidance

## Slide 43
Number porting sets the migration calendar; emergency calling sets the safety floor
Ports move in carrier time — weeks, not days. Emergency-location rules are legal obligations, not product features.
The porting path — six steps, one controlling date
1 · Inventory every DID, toll-free, fax and analog line, with verified ownership
2 · LOA + CSR letter of agency and customer service record filed with the gaining carrier
3 · FOC date firm order commitment — the only date that matters; plan waves around it
4 · Port window usually early morning; numbers cut in batches, with carrier escalation on standby
5 · Verify inbound and outbound on every range, caller ID / CNAM, toll-free, fax
6 · Disconnect old service only after the ported ranges prove stable for a full business cycle
Emergency calling — design duties per platform
On-premises: map emergency response locations (ERL) to ELINs; update ALI records on every move so the PSAP receives a dispatchable address.
Webex Calling: locations carry emergency settings; soft-phone users resolve location dynamically (HELD-based). Administrators define workspace locations explicitly.
Test with 933 (US) after every location or ERL change — it reads back the address the PSAP would see, without dispatching responders.
The legal floor (US)
Kari's Law: direct 911 dialing — no prefix — plus on-site notification to a central point. RAY BAUM'S Act: a dispatchable location must accompany every 911 call, including from soft clients.
Other jurisdictions impose equivalent duties — verify before every country wave.
Why ports slip: CSR mismatches, address mismatches, and pending orders on the losing account cause most rejections — audit the CSR against the invoice before filing the LOA.
Basis: carrier number-porting practice (LOA / FOC); Kari's Law and RAY BAUM'S Act; Webex emergency-calling documentation

## Slide 44
Coexistence is the migration state: one directory, one dial plan, two call-control homes
Users move in waves; routing, voicemail, and directory must behave as if nothing changed.
The hybrid dial plan — four rules that keep calls short and cheap
1 · Normalize to +E.164 end to end on both platforms, so any user is reachable by one canonical number regardless of home system.
2 · Prefer a dedicated SIP trunk between CUCM (via CUBE) and Webex Calling for inter-platform calls; the PSTN is the fallback, not the primary path.
3 · Use steering digits or site codes only where number ranges genuinely overlap; overlapping DIDs are a design smell to fix in the inventory phase.
4 · Keep pilot users reachable at their old number until the port completes.
CUCM users
CUBE
Webex Calling
dedicated SIP trunk, TLS
Route CUCM ↔ Webex calls over the direct trunk first; overflow to PSTN only on trunk failure — hair-pinning through the carrier adds cost and double media anchoring. Measure trunk utilization per wave: it saturates first as waves grow.
Services that must not fork during coexistence
Service | Coexistence rule
Voicemail | Unity Connection serves CUCM users; cloud voicemail serves moved users — MWI follows the user's home system
Directory | one LDAP / AD source feeds both platforms; never maintain two directories
Meetings / IM | Webex app fronts both call-control homes; calling mode set per user
Move users, not features
Recreate only what is used: call-park slots, pickup groups, and hunt pilots with zero calls in 90 days do not migrate — document them as retired. Usage data from CDR / CMR decides, not recollection.
Decommission rule: retire a legacy component only when it has zero users and zero dependencies — verify with reports, not with silence.
Basis: Webex Calling and CUCM hybrid deployment guidance; directory-sync and voicemail coexistence documentation

## Slide 45
A 6–12 month migration runs in five phases, each closed by a gate
Illustrative schedule for a 3,000-user enterprise; compress or stretch to your change windows and porting FOC dates.
1 · Assess
M0–M1
inventory, dependency map, network readiness
2 · Design
M1–M3
locations, dial plan, security review, LOAs filed
3 · Pilot
M3–M5
5% of users — IT plus volunteers; measured exit
4 · Waves
M5–M10
200–400 users per wave, ports per FOC date
5 · Decommission
M10–M12
trunks, gateways, servers, contracts
The gates between phases — objective, signed, and reversible to a No-Go
Gate 1 → Design
readiness report signed; QoS and bandwidth gaps funded and scheduled
Gate 2 → Pilot
design freeze; FOC dates in hand; pilot group and success metrics agreed
Gate 3 → Waves
pilot exit criteria met — MOS ≥ 4.0, no open Sev-1, support staffed
Gate 4 → Decommission
every wave stable two business cycles; rollback path exercised, not assumed
Waves are sized by support capacity, not by ambition: the help desk, floor walkers, and carrier-escalation coverage set the wave size. A wave that generates more tickets than the desk absorbs is too big — halve it and re-gate.
Run rollback as a routine, not an emergency: every wave keeps its legacy configuration intact and its old numbers forwardable until the wave exits. The rollback drill — re-point a user, verify a call, restore voicemail — is rehearsed in the pilot so it takes minutes, not an incident bridge.
Illustrative schedule — phase durations and wave sizes are planning assumptions to be validated per organization

## Slide 46
The honest platform comparison is five-year TCO, not sticker price
Illustrative model for a 2,800-user estate, indexed so the structure is visible — replace every figure with your own quotes before deciding.
Five-year cost structure (indexed, on-prem = 100 per line)
Cost line | On-prem CUCM | UCM Cloud | Webex Calling
Hardware + data center | 100 (refresh yr 4) | ~0 | ~0
Licenses / subscription |  | ~110 | ~120
Upgrade and patch labor |  | ~30 | ~10
Admin staffing | 100 (largest line) | ~60 | ~40
PSTN / trunks |  | ~100 | ~100 (unchanged)
Analog edge (ATA / VG) |  | ~100 | ~130 (more adapters)
Indices are illustrative, not quotes. The shape is the lesson: subscription platforms move spend from capex and labor into per-user opex, while PSTN cost barely moves in any model — anyone promising PSTN savings is selling a trunk consolidation, not a platform.
Where each model actually wins
Cloud wins when
growth is spiky, sites are many and small, IT staff is thin, and the dial plan is standard — labor dominates TCO and cloud deletes labor
On-prem wins when
analog density is heavy, data residency is strict, the data center is already amortized, or the dial plan is genuinely complex
The hidden lines
admin staffing is the largest line and the most ignored; downtime risk needs a number — expected incident cost per year, not a feeling
Model rule
TCO = capex + 5 × opex + labor + risk. Anything you cannot price becomes an assumption line with a name and an owner — an unpriced assumption is how migration business cases fail audits.
Illustrative indices for structure only — not vendor pricing; model with your own quotes, staffing rates and PSTN contracts

## Slide 47
06
Operations & Troubleshooting
Voice engineering never ends at cutover: the monitoring loop, signaling and media fault chains,
and the disaster-recovery and upgrade discipline that keeps the platform boring.
Section 06 of 07 · Enterprise Voice with Cisco

## Slide 48
Expert practice is a loop: design, deploy, operate, optimize — with telemetry throughout
Each stage feeds the next; CDR/CMR and RTMT data collected in "operate" is the evidence base for the next design cycle.
1 · Design
SRND-based sizing; cluster and site model; codec/CAC policy; numbering plan; security baseline
2 · Deploy
BAT bulk provisioning; device-pool templates; staged gateway cutovers; registration verification
3 · Operate
RTMT alarms; CDR/CMR quality review; backup (DRS); patching; capacity watch per subscriber
4 · Optimize
codec & QoS tuning from CMR data; dial-plan cleanup; upgrade windows; cloud-migration re-assessment
telemetry and quality data feed the next design cycle
The troubleshooting toolbox
Tool | Use it for
RTMT | alarms, perf counters, trace & log collection
SDL / SDI traces | call-setup logic failures inside CUCM
Packet capture | one-way audio, NAT, QoS marking issues
CDR / CMR | MOS, jitter, loss per call; abuse and pattern audits
Skill path that structures the expertise
CCNA — networking fundamentals every voice design assumes: VLANs, QoS, routing.
CCNP Collaboration (CLCOR + concentration) — CUCM, gateways, QoS, contact center or cloud specialty exams.
CCIE Collaboration — expert-level design and troubleshooting across the full stack covered in this deck.
Basis: Cisco CUCM serviceability and RTMT documentation; Cisco certification portfolio, cisco.com, early 2026

## Slide 49
RTMT is the first pane of glass: alarms, counters, and traces in one loop
The Real-Time Monitoring Tool ships with CUCM; the expertise is knowing which counter answers which question.
From question to counter — where to look first
Question | Where RTMT answers it
Is the cluster healthy? | service activation per node; DB replication state (utils dbreplication runtimestate)
Are devices registering? | registered-device counters per node; registration-rejected alarms
Are calls completing? | calls attempted vs completed; CDR cause codes for failures
Is a trunk saturating? | active calls per trunk; busy-out events; gateway CPU / DSP
Is media suffering? | CMR per call — jitter, latency, loss, MOS
Is voicemail / IM&P lagging? | companion-node service states; queue depth counters
Collect by device, not by cluster: SDL traces from every node at debug level will drown the signal and load the publisher. Trace the smallest scope — one phone, one trunk — that reproduces the fault.
The alarm-to-evidence loop
1 · Alert rule fires
thresholds on counters → email / syslog to the NOC
2 · Collect traces
Trace & Log Central pulls SDL / CCM traces for the window
3 · Correlate
timestamp + calling number + device name joins alarm, trace, and CDR into one story
Baseline before incidents
Capture a normal week of perfmon counters — registrations, call rates, trunk occupancy, CPU. Every threshold alarm is meaningless until you know what ordinary looks like on your cluster.
Centralized syslog plus CDR analytics close the loop for long-term trend and charge-back reporting.
Basis: Cisco RTMT and CUCM serviceability documentation; counters and alarm workflow per SRND operations guidance

## Slide 50
Signaling faults follow a decision chain: register, route, ring — in that order
Work the chain upstream-first; most call failures originate earlier than where the symptom appears.
The three links of the signaling chain
1 · Registration
power and voice VLAN → DHCP option 150 → TFTP config → registered to the right node? Verify on CUCM, not on the phone display.
2 · Routing
dialed digits → CSS / partition permits? → route pattern → route list → gateway or trunk member up and selected?
3 · Media negotiation
regions agree on codec? → MTP / transcoder available if needed? → SRTP capability matches on both ends?
DNA is the shortcut: Dialed Number Analyzer simulates a call from any device to any digit string and returns the exact routing decision — CSS hit, pattern matched, gateway chosen — without placing a call. Use it before touching the gateway.
Symptom → likely cause → first check
Symptom | Likely cause | First check
reorder tone after dialing | CSS / partition blocks the pattern | DNA with the device's CSS
call drops at connect | codec / DTMF mismatch | regions; MTP allocation
rings once, then fails | gateway dial-peer mismatch | debug voip ccapi inout
registration rejected | CTL / security, wrong CUCM group | phone status messages
inbound PSTN fails | trunk CSS, called-party transform | gateway inbound dial-peer
Read CDR cause codes before debugging: cause 1 = unallocated number, 17 = user busy, 21 = call rejected, 38 = network out of order — the code usually names the link of the chain that broke.
Basis: CUCM DNA and SDL troubleshooting guides; ISDN Q.850 cause codes; IOS voice debug command references

## Slide 51
Media faults announce themselves: one-way audio, choppiness, echo — each has a fingerprint
Read the CMR before touching the network — per-call jitter, loss, and latency numbers name the culprit.
The five fingerprints, confirmed and fixed
Symptom | Most likely cause | Confirm with | Fix
one-way audio | routing asymmetry, ACL or NAT blocks one RTP direction | CMR shows packets in one direction only | fix route / ACL; verify media anchoring on CUBE
choppy, robotic voice | jitter or loss on a congested link | CMR jitter 30 ms or loss 1% | LLQ for EF; fix congestion; check duplex mismatches
echo | acoustic coupling or tail-circuit echo on PSTN | user report; gateway echo-canceller stats | tune echo-canceller coverage; reduce gain levels
delay, talk-over | one-way latency beyond 150 ms | CMR round-trip; path trace both directions | shorter path; remove double media anchoring
DTMF digits lost | interworking mismatch — RFC 2833 vs in-band vs KPML | fails on IVR but voice is fine | align dtmf-relay on both dial-peer legs
CMR is the per-call X-ray: every call writes Call Management Records with jitter, latency, loss, and a computed MOS. MOS ≥ 4.0 is toll quality; below 3.5 users will complain — investigate before they do.
Why one-way audio dominates: media flows end-to-end and ignores the signaling path. Any stateful device — firewall, NAT, asymmetric route — between the RTP endpoints can silently drop one direction while signaling stays healthy.
Basis: CUCM CMR field definitions and MOS thresholds; ITU-T G.114 budgets; IOS DTMF interworking documentation

## Slide 52
Disaster recovery and upgrades are rehearsed procedures, not events
DRS backups, a strict upgrade order, and a tested rollback separate professional operations from incident reports.
DRS — the backup discipline
Schedule nightly backups to an off-box SFTP target — full cluster configuration; CDR / CMR optional by size. Keep multiple generations.
Restore the publisher first, then subscribers rejoin and re-sync. A cluster restore is a planned maintenance activity, not improvisation.
Test restores quarterly. A backup that has never been restored is a rumor, not a recovery plan — prove it in a lab or on a staging publisher.
Store credentials and license files with the backup set; a restore without licenses is half a recovery.
Recovery time is a design input: with a warm standby publisher and verified backups, cluster recovery is measured in hours; without them it is measured in days. Write the RTO into the DR plan and rehearse against it.
DRS covers CUCM, IM&P, and Unity Connection. Contact center platforms and IOS gateways keep their own backup paths — UCCX backup schedules and gateway config archives belong in the same runbook.
The upgrade order — six steps, no improvisation
1 · Read the compatibility matrix UCCX, CUC, IM&P, Expressway, and CUBE versions interlock — plan one window
2 · Backup and snapshot fresh DRS backup plus VM snapshot before any package is staged
3 · Publisher first, then subscribers one at a time; verify replication before moving on
4 · Switch version in the window phones re-register — stagger device pools to control the registration storm
5 · Verify per site dbreplication, registered devices, test calls inbound and outbound
6 · Keep the inactive partition as rollback switching back takes minutes; do not delete the old version until the soak period ends
Basis: CUCM DRS administration and upgrade guides; Cisco compatibility matrix for UC applications

## Slide 53
Working with Cisco TAC is a skill: the evidence package decides the clock
A well-built service request converges in days; a vague one loops for weeks — the difference is the first upload.
Severity and evidence — the two things you control
Severity | Meaning | Use when
P1 / P2 | network down / severe degradation — phone, not email | cluster down, trunk down, site offline; be ready to work the case continuously
P3 | impaired but working | degraded features, workarounds exist, single-site anomalies
P4 | questions, cosmetic, documentation | behavior clarification, config review requests
Honest severity gets honest response: inflating a P3 into a P1 buys one fast pickup and a slower case — TAC re-queues what the evidence does not support, and your next real P1 inherits the doubt.
The first-upload evidence package
□ Problem statement with exact timeline and scope — users, sites, since when, what changed
□ RTMT logs for the incident window, per affected node
□ SDL traces scoped to one failing call, with its Call-ID
□ Packet capture at the failing boundary, if media or trunk related
□ Sanitized configs and a one-page topology diagram
Escalation paths that actually move a case
Path | When and how
Bug Search first | check for a known defect before opening — a published bug ID with a workaround beats a new case
Duty manager | stalled cases, unresponsive queues, missed callbacks — request through the case notes or hotline
Account team | chronic issues, TAM / SE engagement, enhancement requests — TAC fixes defects, account teams move roadmaps
Bug ID literacy | read CSCxx12345 for affected and fixed-in versions before any upgrade — it is the cheapest regression test
The reproduction rule
TAC moves fastest when you can reproduce the fault on demand. Invest in the smallest lab that reproduces it (Section 07) — a reproducible defect is a defect with a countdown clock.
Expectation hygiene: TAC restores documented behavior; it does not redesign your dial plan, and it cannot see your network. The more of Section 06's telemetry you bring, the more the case is diagnosis instead of archaeology.
Basis: Cisco TAC service-request handling and severity definitions; Bug Search Tool usage — operational practice, not an official SLA

## Slide 54
Case study: forty minutes from 'calls sound robotic' to root cause
Illustrative timeline built from a common real-world pattern — the tools and their order are the point, not the site names.
The timeline — every step uses one tool from Section 06
Time | Observation / action | Tool
T+0 | Site B reports robotic, choppy voice on external calls | help desk ticket
T+5 | CMR pull: jitter 45 ms on Site B calls only; MOS 3.2 — the fault is one site, media-plane | CDR / CMR analytics
T+12 | Site B WAN trunk at 98% utilization since morning; LLQ policy intact | RTMT perfmon
T+20 | uplink flapping — err-disable storm after a morning switch change; traffic pinned to one member link | switch logs / syslog
T+32 | traffic shifted to redundant path; queueing verified on the surviving link | runbook procedure
T+40 | MOS back to 4.2 on fresh CMR sample; monitoring watch set for 24 h; change record opened for the storm guard gap | CMR verification
Notice what never happened: no phone reboots, no codec changes, no gateway restarts — the first three queries located the fault before a single device was touched.
What made forty minutes possible
A baseline existed
98% utilization was obviously abnormal because normal was measured last month (RTMT page)
CMR answered in one query
jitter + one site + MOS number turned a feeling into a location — the media-fault page's first move
The runbook had the steps
evidence collection was a checklist, not improvisation — no time spent deciding what to collect
The retrospective question that matters
Which step took longest, and what would make it zero? Here, automated CMR alerting on jitter > 30 ms would have cut detection from T+5 to T+2 — before the ticket existed.
Every incident either buys automation or buys a scar. Prefer automation.
Illustrative timeline — composite of common troubleshooting patterns, not a specific customer incident

## Slide 55
07
Expert Practice & Roadmap
Certification path, operational checklists, capacity planning, and the vocabulary that makes it all precise.
Section 07 of 07 · Enterprise Voice with Cisco

## Slide 56
The certification ladder maps to the job ladder: CCNA → CCNP → CCIE
Each rung adds design authority; hands-on lab time is what turns the ladder into real skill.
Three rungs, three levels of authority
Rung | What it certifies | Role it unlocks
CCNA (200-301) | networking fundamentals incl. QoS and voice basics | operations, first-line voice support
CCNP Collaboration | core CLCOR 350-801 plus one concentration (CLICA, CLACCM, CLCEI, CLAUTO) | design and implementation engineer
CCIE Collaboration | expert written plus full-day practical lab | architecture authority, complex migrations
Concentration choice follows the job: CLICA for implementation depth, CLACCM for advanced call control and mobility, CLCEI for contact-center engineers, CLAUTO for automation and APIs.
Typical pacing — illustrative, not a promise: CCNA in 6–9 months of study, CCNP in 9–12, CCIE over 2–4 years of deliberate practice.
The lab is the difference
Build the smallest real cluster
CML / EVE-NG with a CUCM evaluation, two IOS XE routers as gateway and CUBE, soft clients as phones
Drill the workflows, not the theory
BAT imports, CSS / partition builds, SRST failover, dial-peer debugging — until each takes minutes
Break it on purpose
kill the WAN, misconfigure a CSS, fill a trunk — then troubleshoot with DNA, CDR, and SDL traces only
Rule of thumb
Every hour of study earns roughly two hours in the lab. Interviews and incidents both test what your hands remember, not what you once read.
Basis: Cisco certification portfolio (CCNA 200-301; CCNP Collaboration CLCOR 350-801 and concentrations; CCIE Collaboration), cisco.com

## Slide 57
Cutovers are won in checklists: pre-cutover, cutover night, day two
Every item has an owner and a timestamp; an unowned item does not exist.
Pre-cutover — the week before
□ DRS backup verified and VM snapshot taken
□ FOC date re-confirmed with the carrier
□ Porting list reconciled against inventory
□ Rollback plan written, owners assigned
□ Test-call script ready — inbound, outbound, toll-free, fax, 933
□ Bridge line and escalation contacts scheduled
□ Help desk briefed with wave roster and FAQ
□ Change freeze on both platforms announced
Cutover night — the window
□ Freeze confirmed — no in-flight changes
□ Numbers port; carrier confirmation logged
□ Test-call script executed site by site
□ RTMT watched: registrations, trunks, alarms
□ Every deviation logged with a timestamp
□ Go / No-Go called at each checkpoint time
□ On No-Go: rollback executed, not debated
□ Status notes to stakeholders on schedule
Day two — hypercare
□ Daily hypercare bridge for a week
□ CMR quality review — every MOS < 3.5 call traced
□ Tickets triaged: site pattern vs one-off
□ Directory, speed dials, photos updated
□ Wave exit report signed by stakeholders
Close out: decommission plan updated, lessons learned written while memory is fresh, next wave re-sized from ticket data.
Operational practice — adapt items and owners to your change-management framework; the structure is the transferable part

## Slide 58
Capacity planning is arithmetic: devices, calls, trunks, agents — four formulas
One worked example end-to-end; the same calculations scale from a branch to an enterprise. Figures are illustrative.
Worked example — 2,800 users, one campus, one contact center
Step | Calculation | Result
Devices | 2,800 users × 1.1 endpoint factor (soft clients, common areas) | ≈ 3,100 devices
BHCA | 2,800 × 4 calls at the busy hour | 11,200 BHCA
Cluster headroom | one subscriber pair rated 40k+ devices | pair suffices, 1:1 redundancy intact
PSTN trunks | 30% of busy-hour calls touch PSTN → 11,200 × 0.3 × 150 s ÷ 3,600 s = 140 erlangs; Erlang B at 1% blocking | ≈ 155 channels ≈ 7 PRIs
Agents | 3,600 calls/day over 8 h, AHT 300 s → 37.5 erlangs; Erlang C for 80/20 service level | ≈ 46 agents on shift
Validate with your own busy-hour data: pull 4–6 weeks of CDRs, find the real busy hour, and re-run the arithmetic. Assumed ratios are planning inputs; measured ratios are design inputs.
The four formulas to memorize
devices = users × endpoint factor
1.05–1.15 covers soft clients and shared phones
erlangs = calls × AHT ÷ 3,600
traffic intensity; AHT in seconds, period in seconds
trunks = Erlang B(erlangs, blocking)
blocked calls cleared — for PSTN capacity, 0.1–1% typical
agents = Erlang C(erlangs, service level)
blocked calls wait — for staffed queues like 80/20 targets
Erlang B vs C in one line: trunks either get a call or the caller hears busy (B); agents either take the call or the caller queues (C). Using the wrong model under-sizes the wrong resource.
Illustrative figures — ratios and busy-hour multipliers are planning assumptions; recompute from measured CDR data before design

## Slide 59
Design documents are the deliverable that outlives the project
Configurations change; the HLD, LLD, as-built and runbook are what the next engineer — often you, two years later — actually needs.
Four documents, four readers, four lifetimes
Document | Contents | Reader
HLD | architecture, sizing, availability model, security zones, key decisions with rejected alternatives | decision-makers, reviewers
LLD | every parameter value — device pools, CSS / partition tables, dial-peer inventory, gateway configs | implementers
As-built | what actually shipped, with diffs from the LLD and why | operations
Runbook | adds / moves / changes, backup and restore, incident playbooks, escalation contacts | support tiers
The rejected-alternatives paragraph is the gold: anyone can read what was built; only the HLD records why the other designs lost. Migrations fail when the new team re-litigates settled decisions because the reasoning was never written down.
What a design review actually checks
□ Every requirement traces to a design decision
□ Capacity numbers cite sources — the Section 07 formulas, not adjectives
□ Rollback is documented per change, not per project
□ Assumptions are labeled, each with a name and an owner
□ Diagrams match configs — a diagram that lies is worse than none
□ Failure domains are drawn: what breaks when each node, link and site dies
Documentation debt compounds
Every undocumented exception is a future incident without context. The cheapest documentation is written during the change window, by the person making the change — afterward it costs ten times more and says half as much.
Store docs where the outage can't reach them — not on the cluster they describe.
Basis: Cisco PPDIOO / design methodology guidance and professional-services documentation practice

## Slide 60
Automation turns configuration into code: AXL, CURRI, CTI, and the Webex APIs
Anything you configure twice by hand is a script; anything you configure per migration wave is a pipeline.
The five interfaces worth learning
Interface | Purpose | Typical use
AXL (SOAP) | CUCM provisioning API | bulk adds beyond BAT, drift audits, configuration as code
CURRI | external routing decisions | CUCM asks your app to allow or route each call — compliance and policy logic
JTAPI / TAPI | CTI call control and events | attendant consoles, screen pops, recording triggers
Webex REST + webhooks | users, locations, devices, queues | migration pipelines, day-two sync with HR systems
Ansible / Terraform | community modules and IOS providers | lab builds, repeatable DR rebuilds, gateway config generation
Start read-only: an AXL script that audits CSS / partition consistency across 10,000 devices pays back before any write script — and it can never break a call. Writes come after the audit habit exists.
A minimal call, end to end
# Webex API — assign a number # to a user (migration wave step) POST /v1/telephony/config/ people/{personId}/numbers Authorization: Bearer { "phoneNumber": "+14085550100", "locationId": "Y2lzY28..." }
The cautions that keep automation safe
· Idempotency — re-running must be safe; check before create
· Rate limits — retry with backoff; batch reads, not one per user
· Secrets in a vault — never in the script, never in git
· Lab first — every write script earns production by running clean in the lab
· Windows still apply — automation accelerates configuration, not judgment
The CCNP CLAUTO concentration (Section 07) formalizes exactly these skills — APIs are now a certification topic, not a hobby.
Basis: CUCM AXL / CURRI / JTAPI developer documentation; Webex for Developers API reference, developer.webex.com

## Slide 61
Appendix · the vocabulary that keeps designs precise
Every acronym used in this deck, in one place — the fastest page to revisit before a design review.
Platforms and call control
CUCM — Unified Communications Manager; on-prem call control
CUC — Unity Connection; enterprise voicemail
IM&P — IM and Presence service, paired with CUCM
CUBE — Cisco Unified Border Element; IOS XE SBC
SBC — session border controller; edge demarcation
SRST — Survivable Remote Site Telephony; branch fallback
Expressway — edge pair (E in DMZ, C inside) for MRA and B2B
MRA — Mobile and Remote Access; VPN-less remote registration
MPP — multiplatform-phone firmware (7800/8800 MPP)
Jabber — desktop / mobile soft client for CUCM
UCCX / UCCE — contact center express / enterprise editions
Finesse — browser agent and supervisor desktop
ECE — Enterprise Chat and Email for UCCE digital channels
Webex Calling — Cisco's cloud call-control SaaS
LGW — Local Gateway; customer PSTN breakout for Webex
Control Hub — Webex administration console
Protocols, media, and operations
SIP / SDP — session setup protocol / media description it carries
RTP / SRTP — media transport / its encrypted form
RFC 2833 / RTP-NTE — DTMF as named telephony events
E.164 — international number format; + prefix form recommended
DID / DDI — direct inward dialing number
PRI — ISDN primary rate interface; 23/30 bearer channels
CSS / PT — calling search space / partition; CUCM permissions
AAR — automated alternate routing on CAC denial
MTP — media termination point; inserts for DTMF / early offer
DSP — digital signal processor; hardware transcoding / conferencing
EF / CS3 — DSCP markings for media / signaling
LLQ — low-latency queuing; priority queue for EF
MOS — mean opinion score; 4.0+ is toll quality
CDR / CMR — call detail / call management (quality) records
RTMT — Real-Time Monitoring Tool
DRS — Disaster Recovery System backups
DNA — Dialed Number Analyzer routing simulator
BHCA — busy-hour call attempts
Contact center metrics: AHT average handle time · ASA average speed of answer · CSQ contact service queue · Erlang B/C sizing models · SL service level (e.g. 80/20) · WFM workforce management · QM quality management
Terminology per Cisco UC documentation and SRND; definitions abbreviated for reference use

## Slide 62
Conclusions: five claims this deck stands behind
Each claim is the title logic of its section, restated; section references point to the evidence pages.
1
Voice quality is engineered, not purchased — codec choice, 20 ms packetization and CAC policy determine call quality before any vendor platform does (Sec. 01).
2
CUCM mastery is object mastery — CSS/partitions for policy, route lists for path preference, device pools for consistency; most outages trace to one of these layers (Sec. 02).
3
Contact center selection is a scale and ownership decision — UCCX to ~400 agents, UCCE for complex enterprise routing, Webex CC when the platform should be someone else's operations problem (Sec. 04).
4
Cloud migration succeeds as gated phases — pilot, wave, port, decommission; the two gates that actually stop projects are number porting and E911, and both are testable in advance (Sec. 05).
5
Expertise is operational, not ceremonial — the design–deploy–operate–optimize loop, fed by CDR/CMR telemetry, is what separates a maintained voice estate from a frozen one (Sec. 06–07).
Open questions for your environment
· Which CUCM features in daily use lack a Webex equivalent?
· What share of devices is analog, fax or legacy SCCP?
· Which countries in scope lack Cisco Calling Plans coverage?
Primary sources
· Cisco Collaboration SRND — cisco.com design guides
· CUCM / Unity Connection / IM&P / Expressway administration guides, cisco.com
· UCCX & UCCE product documentation, cisco.com
· Webex Calling & Contact Center documentation, help.webex.com
Enterprise Voice with Cisco — Technologies, Contact Center & Cloud Migration · capability statements reflect documentation current as of early 2026